## Slide 1: TxDOT Research Project 0-7150: Artificial Intelligence for Pavement Condition Assessment from 2D/3D Surface Images
Project Update Meeting #5
11/04, 2024

## Slide 2: AGENDA
1
2
3
Tasks Overview
Task 5 updates
4
Future Work
Q & A

## Slide 3: Research Tasks
Project Management
Review Literature on Pavement Condition Assessment and Artificial Intelligence
Establish a Library of Pavement 2D/3D Images in AASHTO Standard Format
Evaluate Current Practices of Pavement Condition Assessment
Develop Machine Learning Based Models for Pavement Distress Measurement
Develop Practical Tools for Pavement Condition Assessment
Pilot Study for Machine Learning Based Pavement Condition Assessment Implementation

## Slide 4: AGENDA
1
2
3
Tasks Overview
Task 5 updates
4
Future Work
Q & A

## Slide 5: Task 5 Description
Dataset preparation
  - Image library revision
  - Data analysis
Crack segmentation
  - AI/ML-based models for ACP, JCP, and CRCP
Crack detection model development
  - AI/ML-based models for ACP and JCP
  - Comparison with PathView
* Developed tools for crack detection using standard format images

## Slide 6: Image library revision
Why revision:
  Barely visible distresses
  Consistency

## Slide 7: Image library revision
3D image
Source: PSI data 2022
(BU0077LL_9.188_7.413)
Collection year: 2021
Collection year: March 2021
Google Street View
31°32'36.6"N 97°06'31.0"W
Cracks not been properly captured by the 2D/3D images
2D image
Source: PSI data 2022
(BU0077LL_9.188_7.413)

## Slide 8: Image library revision
PSI ratio
Actual spatial ratio
The unfixed spatial ratio may impact the identification of certain distress classes such as Transverse crack
Transverse resolution 2.75 mm
Longitudinal resolution 6.97 mm

## Slide 9: Image library revision
3D image
Why revision:
  Different interpretation by individual annotators

## Slide 10: Image library revision
Annotation 1
Why revision:
  Different interpretation by individual annotators

## Slide 11: Image library revision
Annotation 2
Why revision:
  Different interpretation by individual annotators
  Both annotations are correct but detection results could be very different

## Slide 12: Image library revision
Why revision:
  Barely visible distresses
  Consistency
Strategy:
  Removed ambiguous annotation
  Modified bounding boxes

## Slide 13: Image library revision
Before revision
After revision

## Slide 14: Two types of tasks
Detection
Segmentation
Input
Longitudinal crack

## Slide 15: Segmentation dataset

## Slide 16: Segmentation
Methods:
  U-Net
  FCN
  PSPNet
  SegNet
FCN
U-Net
PSPNet
SegNet

## Slide 17: Performance Metrics
Main metrics:
  Precision: in the aspect of False positive
  Recall: in the aspect of False negative
  F1: a balanced indicator between precision and recall
All metric scores range from 0 to 1, with higher values indicating better performance.

## Slide 18: Segmentation - ACP
All models show close performance, with F1 score (mFscore) around 77% across the board
FCN-WCE achieves the highest F1-score (mFscore = 77.78) and precision (81.57)

## Slide 19: Segmentation - ACP
Good Performance with Clear Cracks:
  Accurate segmentation for clear, well-defined cracks with distinct boundaries.
Poor Performance with Sealed and Alligator Cracks:
  Incomplete or fragmented detection for sealed and complex alligator cracks.
False Positives Due to Complex Background

## Slide 20: Segmentation - JCP
All models show close performance, with F1 score (mFscore) around 90% across the board
PSPNet-WCE achieves the highest F1-score (mFscore = 92.24)
Performance is significantly better than that of ACP

## Slide 21: Segmentation - JCP
Good Performance with Clear Cracks:
  Accurate segmentation for clear, well-defined cracks with distinct boundaries.
Poor Performance with thin cracks:
  Incomplete or fragmented detection for thin cracks.
Much less False Positives compared to ACP

## Slide 22: Segmentation - CRCP
All models show close performance, with F1 score (mFscore) around 77% across the board
PSPNet-WCE achieves the highest F1-score (mFscore = 78.99)
Performance is similar compared to ACP, significantly lower than JCP

## Slide 23: Segmentation - CRCP
Good Performance with Clear Cracks:
  Accurate segmentation for clear, well-defined cracks with distinct boundaries.
Poor Performance with Sealed and Thin Cracks:
  Incomplete or fragmented detection for sealed and thin cracks.
False Positives Due to Complex Background

## Slide 24: Segmentation
Summary:
  Better performance with JCP (92.24%), compared to ACP (77.78%) and CRCP (78.99%)
  Small sample size
  Additional steps needed to satisfy TxDOT’s requirement

## Slide 25: Distress Detection
After revision, a total of 12,123 images for distress detection are adopted for AI/ML model training.
Annotation type | Pavement Type | Number of annotated images
Detection (Bounding box & distress class) | ACP | 5,201
McLennan | JCP | 6,922
Harrison | CRCP | -
Detection Annotation Summary

## Slide 26: ACP Detection dataset
Train : Validation : Test = 70% : 15% : 15%
Imbalanced dataset
Block cracks and Potholes and others under 200

## Slide 27: JCP Detection dataset
Train : Validation : Test = 70% : 15% : 15%
Imbalanced dataset
7 distress classes with instance number under 200

## Slide 28: Distress Detection
Methods:
  One-stage methods (YOLO)
  Two-stage methods (Faster R-CNN)

## Slide 29: Distress Detection
Proposed methods:
  MoPac
  Attention-based neural network

## Slide 30: Performance Metrics
Main metrics:
  Precision: in the aspect of False positive
  Recall: in the aspect of False negative
  F1: a balanced indicator between precision and recall
  mAP: a more comprehensive metric, considering the model's precision and recall across multiple thresholds

## Slide 31: Detection - ACP
Experiment setting:
YOLOv5s(setting 1) : Original size + single channel input + anchor
YOLOv5s(setting 2) : Original size + single channel input
YOLOv5s(setting 3) : Reduced size + three-channel input + anchor

## Slide 32: Detection - ACP
Performance:
YOLOv5s(setting 3) yielded the best mAP (0.64) by a large margin
YOLOv8 performed worse than YOLOv5
Faster RCNN yielded the lowest performance

## Slide 33: Detection - ACP
High mAP50 scores for Joint, Lane longitudinal, and Sealed longitudinal
Lower mAP50 scores for classes like Pothole (0.23), Longitudinal (0.44), and Transverse (0.56)
Not enough sample
Barely visible cracks?

## Slide 34: Detection - ACP
Combined Image Types:
Achieves highest overall performance across metrics
Precision: 0.71 | Recall: 0.702
mAP50: 0.72 | mAP50-95: 0.383
Insight:
Merging intensity and range images enhances YOLOv5s detection accuracy effectively

## Slide 35: Detection - ACP
Observations:
Majorities of distress classes improved
Performance of Transverse crack detection drops
mAP50 of Transverse and Longitudinal cracks are still below 0.7

## Slide 36: Detection - ACP
Propose model:
Significantly improved the performance of Transverse and Sealed transverse detection
Caused a slight performance drop of other distress classes
Further actions required

## Slide 37: Detection – ACP (latest progress)
A new dataset (Data v3) developed by adding a small portion of 2023 psi data into the original dataset (2022 psi data):
Detection performance of all distress classes improved
All mAP scores passed 0.7 except Pothole (still not enough sample)

## Slide 38: ACP detection sample

## Slide 39: Detection - ACP

## Slide 40: Detection - ACP

## Slide 41: Detection - ACP
Missing detection

## Slide 42: Detection - ACP
Missing detection

## Slide 43: Detection - ACP
Wrong detection

## Slide 44: Detection - JCP
Experiment setting:
YOLOv5s(setting 1) : Original size + single channel input + anchor
YOLOv5s(setting 2) : Original size + single channel input
YOLOv5s(setting 3) : Reduced size + three-channel input + anchor

## Slide 45: Detection - JCP
Experiment setting:
YOLOv5s(setting 3) yielded the best mAP (0.53)
YOLOv8 performed significantly worse than YOLOv5
Faster RCNN yielded the lowest performance

## Slide 46: Detection - JCP
Key observations:
-mAP50 exceeds the 0.7 threshold for most classes
The rest of classes have the mAP of 0.0
Insight: underrepresented distress classes
Not enough sample

## Slide 47: Detection - JCP
Observations:
Using only intensity images yielded the best performance (different from ACP)
Precision: 0.82 | Recall: 0.84
mAP50: 0.87
Insight:
Most distresses are visible in the intensity image alone

## Slide 48: Detection - JCP
Observations:
Using both intensity and range image does not significantly improve the performance
Using intensity only is better than using range only (very interesting)
More data may be needed

## Slide 49: Comparison with PathView
Factors contributing to difference (according to manual visual check):
Wrong detection/classification
Different perceptions of cracks
Different data postprocessing

## Slide 50: Comparison with PathView

## Slide 51: Comparison with PathView
PathView
Proposed method
Source: SH0347_R_10.819_11.338
False
negative

## Slide 52: Comparison with PathView
PathView
Source: SH0347_R_10.819_11.338
Proposed method
False
Class

## Slide 53: Comparison with PathView

## Slide 54: Comparison with PathView
PathView
Source: SH0073_R_8.234_13.818
Proposed method
False
class
False
class
False
positive

## Slide 55: Comparison with PathView
PathView
Source: SH0073_R_8.234_13.818
Proposed method
False
class
False
negative

## Slide 56: Comparison with PathView
PathView
Source: SH0073_R_8.234_13.818
Proposed method
False
negative
False
positive

## Slide 57: Comparison with PathView
PathView
Source: SH0073_R_8.234_13.818
Proposed method
False
negative
False
positive
False
positive

## Slide 58: Comparison with PathView
PathView
Source: SH0073_R_8.234_13.818
Proposed method
False
positive
False
positive

## Slide 59
Distress Detection Tool (Demo)

## Slide 60: AGENDA
1
2
3
Tasks Overview
Task 5 updates
4
Future Work
Q & A

## Slide 61: Future Work
Milestone
Next Step?
We are here

## Slide 62: Future Work
Task 6
Complimentary data annotation
Further model development

## Slide 63: AGENDA
1
2
3
Tasks Overview
Task 5 updates
4
Future Work
Q & A

## Slide 64: Q & A